## Slide 1: AROF API
Protocol:
  REST
AROF Configuration:
  Laser 1 on/off
  Laser 2 on/off
  Laser 3 on/off
  Laser 4 on/off
AROF Monitoring:
  No parameter

## Slide 2: AROF API
POST/PUT (Configuration of operations):
  Post/put ('http://localhost:5001/api/arof/arof_id’)
  Description: Configuration of the operations in the laser
  operations: {laser_enable: boolean (true | false), “arof_id”:number value}
  Responses:
    200: "description": "Successful configuration”
    400: "description": "Invalid input params“
GET (status of configured operations):
  get('http://localhost:5001/api/arof/’)
  Description: Request of the operations configured in the laser
  Responses:
    200: "description": "Successful configuration”
      Operations
    400: "description": "Operations not found“

## Slide 3: AROF API
DELETE (delete configuration of operations):
  delete ('http://localhost:5001/api/arof/[arof_id]’)
  Description: removal of the operations configured in the laser
  Responses:
    200: "description": "Successful deletion”
    400: "description": " Invalid input params“

## Slide 4: Test
AROF agent 1 Post laser 1 (off)
AROF agent 1 Post laser 2 (off)
AROF agent 1 Post laser 3 (off)
AROF agent 1 Post laser 4 (off)
AROF agent 1 Put laser 1 (on)
AROF agent 1 Put laser 2 (on)
AROF agent 1 Put laser 3 (on)
AROF agent 1 Put laser 4 (on)
AROF agent 1 GET
AROF agent 1 Put laser 1 (on)
AROF agnet 1 Put laser 2 (on)
AROF agent 1 GET
AROF agent 1 delete laser 1
AROF agent 1 delete laser 2
AROF agent 1 delete laser 3
AROF agent 1 delete laser 4

## Slide 5: OBFN API
Protocol: REST
4xOBFN Configuration:
  Reference wavelength
  Beam 1 X Offset Angle (deg): [-90,90]
  Beam 1 Y Offset Angle (deg): [-90,90]
  …
  Beam 4 X Offset Angle (deg): [-90,90]
  Beam 4 Y Offset Angle (deg): [-90,90]
OBFN Monitoring:
  Parameters configured.

## Slide 6: OBFN API
POST (Configuration of operations):
  post ('http://localhost:5002/api/obfn/’)
  Description: Configuration of the operations in the beams
  operations: [{“X_offset_angle”: number value, “Y_offset_angle”:number value, “beam_id”:number value},…]
  Responses:
    200: "description": "Successful configuration”
    400: "description": "Invalid input params“
GET (status of configured operations):
  get('http://localhost:5002/api/obfn/’)
  Description: Request of the operations configured in the beams
  Responses:
    200: "description": "Successful configuration”
      Operations
    400: "description": "Operations not found“

## Slide 7: OBFN API
PUT (replace the configuration of operations):
  put ('http://localhost:5002/api/obfn/[beam_id]’)
  Description: reconfiguration of the operation in the beams
  operations: {“X_offset_angle”: number value, “Y_offset_angle”:number value, “beam_id”:number value}
  Responses:
    200: "description": "Successful reconfiguration”
    400: "description": "Invalid input params“
DELETE (delete configuration of operations):
  delete ('http://localhost:5002/api/obfn/’)
  Description: removal of the operations configured in the beams
  Responses:
    200: "description": "Successful deletion”
    400: "description": " Invalid input params“

## Slide 8: Test